## Slide 1: Next Gen EDSFF All Flash Storage Platform and CXL Solutions
July 2023
Patrick Chiu, Sr Dir of Product Management
Calbert Lo, Manager of Product Management

## Slide 2: Agenda
EDSFF storage product evolution
Next Generation EDSFF platform Innovation
E3.S 2T CXL system management challenges

## Slide 3: Benefits of EDSFF SSDs
For Both System Architects/Designers and Data Center End-Users
Capacity Scaling
Wider PCBs for more flexible NAND Chip layouts
Thermal Efficient
Improvements for thermal and cooling management
Solution Range
Wild range of power profiles (20W - 70W) for higher capacity/performance SSDs, SCM and networking
Performance Scaling
Scalable Connector Design, Multiple Link widths (x4, x8, x16) and support different power profiles
Future Proofed
Common connector for all form factors and more robust signal integrity for future PCIe generations
EDSFF E1.L
EDSFF E3
EDSFF E1.S

## Slide 4: NVMe SSD Form Factor Comparison
U.2
Thickness: 7.0mm/15.0mm
Max Power: 25W
69.85mm
100.45mm
x4 only
E1.S
Thickness: 5.9mm / 8.01mm
Max Power: 12W/16W
E1.S
Thickness: 9.5mm/15.0mm/25.0mm
Max Power: 20W/20W/25W
33.75mm
118.75mm
x4 / x8
31.5mm
110.49mm
x4 / x8
22.0mm
x4 only
42
60
80
110
110.0mm
M.2
Thickness: 4.3mm MAX
Max Power: 8W
E1.L
Thickness: 9.5mm/18.0mm
Max Power: 25W/ 40W
38.4mm
318.75mm
x4 / x8
*Reference: 3.5” HDD Dimension: 147mm x 101.6mm, thickness: 25.4mm/26.1mm
E3.S/2T
Thickness: 7.5mm/16.8mm
Max Power: 25W/40W
E3.L/2T
Thickness: 7.5mm / 16.8mm
Max Power: 40W/ 70W
112.75mm
76.0mm
x4 / x8 / x16
E3.L
E3.S
142.2mm

## Slide 5: SMC EDSFF Storage Platform Release Timeline
18’
23’
22’
19’
PCIe Gen5 E3.S (CXL)
PCIe Gen5 E1.S
PCIe Gen3 E1.S & NF1
Intel CLX DP, 165W TDP
24 DIMMs DDR4
2 PCIe x16 HHHL slots
PCIe Gen3 E1.L
Industry Leader for the EDSFF All-NVMe SSD Platforms
Intel CLX DP, 205W TDP
24 DIMMs DDR4
2 PCIe x16 FHHL slots
1 PCIe x4 HHHL slots
Intel SPR DP, 280W TDP
32 DIMMs DDR5
2 PCIe x16 OCP 3.0 slots
2 PCIe x16 FHHL slots
Intel SPR DP, 350W TDP
32 DIMMs DDR5
AMD Genoa UP, 380W TDP
24 DIMMs DDR5
2 PCIe x16 OCP 3.0 slots
2 PCIe x16 FHHL slots

## Slide 6: EDSFF Storage Platform Adoption
Eco System Support
From Hyperscalers only to all Enterprise and Data Centers
Hardware Readiness
  PCIe Gen5 processor supports more PCIe lanes and higher cores
  Data center networking infrastructure upgrade from 100Gb/s to 200Gb/s to 400Gb/s
2019
2023
80 PCIe Lanes
64 cores
128 PCIe Lanes 128 cores

## Slide 7: Gen5 Petascale EDSFF Platform Innovation
Unified Chassis
  One chassis supports both Intel and AMD, 1U up-to 16 E3 SSD and 2U up-to 32 E3 SSD
  Less than 32” depth
Balanced Architecture
  Balanced PCIe lanes design for both storage IO and networking and eliminates the processor NUMA challenges
Purposed Built for New All-NVMe and Software-Defined Data Center
x64
x64
AMD Single Processor
Intel Dual Processor
x32
x48
x32
x48
< 32” chassis depth
1U16, 2U32 and CXL

## Slide 8: Gen5 Petascale EDSFF Platform Innovation
Signal Integrity
  Mainboard direct connection to SFF-TA-1002 1C connectors and reduce the SSD backplane routing signal loss
  Reduce ~40% of the signal loss
Air Flow
  No vertical SSD backplane blocking the air flow
  ~ 75% increase front opening
  ~ 20% improve system CFM
Reduce Backplane Trace Layout Signal Loss & Improve Air Flow
E3.S SSD + BPN
U.2 SSD + BPN
Notes: MCIO to MCIO cables about 7db, BPN trace layout takes 4 to 5 db loss,

## Slide 9: X13 Intel Based Petascale Flexible Topology
Total 160 PCIe 5.0 IO Lanes and Provide Balanced Front Storage and Rear IO Bandwidth in 1U Design
Subject to change without notice
AMD
x64
x64
1U 16x E3.S SSD (x4)
PCIe
PCIe
Ultra High Performance Storage
UPI
SPR
SPR
OCP
OCP
x64
x64
1U 8x E3.S SSD (x4) &
4x E3.S CXL (x8)
CXL
PCIe
PCIe
High Performance & Memory Hybrid Storage
UPI
SPR
SPR
OCP
OCP
x96
x64
2U 24x E3.S SSD (x4)
PCIe
PCIe
Ultra High Performance and Balanced Storage
UPI
SPR
SPR
OCP
OCP
OCP
OCP
x128
x32
2U 32x E3.S SSD (x4)
High Performance and Density Storage
UPI
SPR
SPR
OCP
OCP
OCP
OCP

## Slide 10: H13 AMD Based Petascale Flexible Topology
The 128 PCIe 5.0 IO Lanes and Provide Balance Front Storage and Rear IO Bandwidth in both 1U and 2U Design
Subject to change without notice
x64
x64
1U 16x E3.S SSD (x4)
AMD
PCIe
PCIe
Ultra High Performance Storage
OCP
OCP
x64
x64
2U 32x E3.S SSD (x2)
AMD
PCIe
PCIe
Petabyte Scale Massive Storage
OCP
OCP
x64
x64
1U 8x E3.S SSD (x4) &
4x E3.S CXL (x8)
CXL
AMD
PCIe
PCIe
High Performance & Memory Hybrid Storage
OCP
OCP
x96
x32
2U 24x E3.S SSD (x4)
AMD
High Performance and Density Storage
OCP
OCP

## Slide 11
PCIe 5.0 Slots 2 x16 slots & 2x AIOMs
X13 1U Petascale All-Flash
Dual Processor Up to 270W TDP
E1.S/E3.S EDSFF Next-gen form factor
DDR5 Slots Up to 32 DIMMs
Optional E3.S 2T x8 CXL Support
Redundant Power Supply 1600W (Titanium level)
PCIe 5.0 Slots x16 AIOMs
PCIe 5.0 Slots x16 slots

## Slide 12
PCIe 5.0 Slots 2 x16 slots & 2 AIOMs
H13 2U Petascale All-Flash
Dual Processor Up to 350W TDP
E3.S EDSFF Up to 32 E3 1T slots
DDR5 Slots Up to 24 DIMMs
Hot swap U.2
PCIe 5.0 Slots x16 AIOMs
PCIe 5.0 Slots x8 or x16 slots
Redundant Power Supply 1600W (Titanium level)

## Slide 13: Petascale All-NVMe Storage Key Advantages
Extreme Performance and Capacity to Support Software-Defined Data Center Workloads
Cooling
Efficiency
New EDSFF connectors and system level design thermal optimization
Applications
flexible
- TLC, QLC and CXL support
- High performance database
- Hyperconverged infrastructure
- AI/MLOps storage
- Virtualization & dense VDI
- High performance Obj storage
Performance
Consolidate
128KB Sequential Read
230+
GB/s
30M+
IOSP
4KB Random Read
Capacity
Consolidate
All-NVMe storage in 2U
*w/ 30TB SSD
1PB

## Slide 14: CXL Memory Module Solutions through Side Band
Compare to NVMe SSD Side Band Capability Versus CXL Devices
NVMe Management Interface (Like)
CCI over Management Component Transport Protocol (MCTP)
MCTP over SMBus/I2C/I3C
SMBus/I2C/I3C
Management Controller
Management Applications
MCTP over PCIe
PCIe VDM
NVMe Management Interface
Management Component Transport Protocol (MCTP)
MCTP over SMBus/I2C
SMBus/I2C
Management Controller
Management Applications
MCTP over PCIe
PCIe VDM
NVMe SSD
CXL Devices
Not As Simple as Just Cooling the CXL Memory Module

## Slide 15: CXL Memory Module Solutions through Side Band
Compare to NVMe SSD Side Band Standard / Common Address Versus CXL Devices
No Unify Address on NVMe MI Like Cmd
No Unify Address on Temperature Reporting
No Unify Address on SMBus
No Unify Address on VPD/SPD
Common Address on NVMe MI
Common Address on Temperature Reporting
Common Address on SMBus
Common Address on VPD
NVMe SSD
CXL Devices
Not As Simple as Just Cooling the CXL Memory Module

## Slide 16: CXL Memory Module Solutions through Side Band
.
xPU
GPU
Network NIC, Smart NIC
Memory Capacity Expansion
Memory Bandwidth Expansion
Type 1: Networking / Caching / Accelerator Devices
Type 2: Accelerator w/ Memory
Type 3: Memory
Storage Class Memory
Protocols
Protocols
Protocols
CXL.io
Protocol Side Band Management
CCI Type 3 + NVMe-MI Like Cmd Set
Protocol Side Band Management
SMBus + SMB w/ PBI
Protocol Side Band Management
NC-SI + PLDM over MCTP
CXL.cache
CXL.io
CXL.mem
CXL.cache
CXL.io
CXL.mem
Coherent (PCIe) Interface and Protocol (CXL) but Still No Unified Device Attributes through Side Band Management Across All Device Types
CXL Device Type
CXL Device Protocol
Existing Side Band Protocol

## Slide 17: Call to Action
Collaborate and build EDSFF eco system
  E1.S and E3.S SSD
  E3.S 2T CXL
Promote the EDSSF based enterprise and data center solutions

## Slide 19
Thank You